## Slide 1: BCSEA Project – Training on IMO PSC procedures for non-MoU on PSC countries
Lisbon/20-21 June 2018
Nikos Katsoulis / Project Officer B.3.1 Training & Co-operation
Directive 2009/16/EC on Port State Control

## Slide 2: Disclaimer
This Presentation is continuously updated and corrected where relevant.
EMSA assumes no responsibility for older versions of slides being used by external parties over which the Agency has no control.
Please note that it cannot be guaranteed that what you will see exactly reproduces an officially adopted text. Only European Union legislation published in paper editions of the Official Journal of the European Communities is deemed authentic.

## Slide 3: Purpose of PSC Directive
To help to drastically on reducing substandard shipping by:
Increasing compliance with international and relevant Community legislation
Implementing a PSC system aiming at the inspection of all ships with a frequency depending on their risk profile
Establishing common criteria for control of ships by PSC & harmonising procedures on inspection and detention

## Slide 4: PSC & International Conventions
4
Load Lines 1966 and Protocol 1988
SOLAS 1974 and Protocols 1978 - 1988
MARPOL 73/78 and Protocols 1978 - 1997
STCW 78/95
COLREG 72
Scope: To verify the compliance of the vessel with the “relevant instruments”:
Bunkers Convention 2001
Tonnage 1969
ILO No147 and Protocol 1996
Civil liability for oil pollution - CLC 92
Anti-fouling Convention (AFS 2001)
Notes: 4

## Slide 5: PSC & International Conventions
5
SOLAS I/19
Check validity of the certificates
If “clear grounds”, actions to ensure the vessel does not sail until it can do so without danger for ……… the ship and her crew
MARPOL Art 5(2)
Check validity of the certificates
If “clear grounds” actions to ensure the vessel does not sail until it can do so without …..presenting unreasonable threat to the marine environment
Load Lines Art 21
Check validity of the certificates
Check the vessel is not overloaded
The port State is authorized to …… ensure the vessel does not sail until it can do so without danger for the ship and her crew
STCW Art X - Reg I/4
Verify that crews are certified as required
Assess the crews’ ability to perform their duties
To detain the vessel if: .........
Notes: 5

## Slide 6: Regional MOU Agreements

## Slide 7: Regional Agreements on PSC
To avoid distortion of the market and to enhance effectiveness
Sharing of information
Common rules
Target for number of inspections
Added value from regional agreements on PSC

## Slide 8: Regional Agreements on PSC
Paris MOU (& other regional agreements on PSC)
Limitations
Gentlemen’s agreement
Partial / No supervision
European Legislation on PSC
Effective supervision
Compliance

## Slide 9: PSC Directive core elements
Core elements as stipulated in the legal text are:
 RoPax references
 Ship Risk Profile
 Inspection frequency
 Postponement
 Over and Under burdened MSs
 Fair Share
 Banning
 Ship Reporting

## Slide 10: References to Ropax in PSC Directive
Recital 22
Reduce Burden for MS
RoPax surveys count as PSC inspections Diff. Flag
Ropax surveys 1. count as PSC inspections MD/EI
2. count for MS commitment
RoPax subject to PSC regime Rectification of deficiencies, Detentions, Banning
Banning
Article 15.3
Article 16.1

## Slide 11: PSC and Ropax Exercise
PSC Directive
PSC
Officer
Ropax
Inspector
PSC
Officer
Ropax Directive
1
2
3

## Slide 12: Basic PSC Process – SRP Calculations
VIMSAS?
Company
Performance
Flag
Performance
RO
Performance
SHIP RISK PROFILE
Ship
Particulars
Inspection
History
Inspections and Performances as per Paris MoU
Notes: VIMSAS - Voluntary IMO Member State Audit Scheme
The List of audited flags is updated when new info becomes available

## Slide 13: Ship Risk Profile
HRS – High Risk Ship
SRS – Standard Risk Ship
LRS – Low Risk Ships
Generic Factors
  Type of Ship
  Age of Ship
  Flag
  RO
  Company
Historical Factors
  Deficiencies
  Detentions
(SRP is recalculated on a daily basis)
Notes: From Submitted or validated inspections
SRP Is Calculated on a daily basis (overnight)
SRP could change during the call! But for the on-going inspection it has no effect

## Slide 14: How will Ship be HRS?
HRS have Weighting points  5
  Ship Type 2 points Chemical, Gas, Oil, Bulk or Passenger Ship
  Ship Age > 12 yrs 1 point
  VHR, HR, and MR to HR Flag 2 points
  MR Flag 1 point
  Very Low or Low RO Performance 1 point
  Very Low or Low Company Performance 2 points
  Detentions in previous 36 months  2 1 point
Example: Oil Tanker, HR Flag and Low RO performance.

## Slide 15: How can Ship be LRS?
Generic Factors
  Ship Type and Age have no influence
  Flag is White and IMO-Audit
  RO is Recognised at least by one PMoU MS and High Performance
  Company is High Performance
Historical Factors
  ≤ 5 deficiencies in each inspection in previous 36 months
  0 Detentions in the previous 36 months
  To have been inspected in previous 36 months
Notes: EU Recognized is for EU MS
Paris MoU prefers to call it “recognized by one or more Paris MoU MS”

## Slide 16: Question
How a SRS is defined

## Slide 17: How to know Flag Performance?
Consult EMSA & Paris MoU website www.parismou.org
Calculated taking in account previous 3 years
Calculated each year Renewed every 1st of July

## Slide 18: How to know RO Performance?
Consult EMSA & Paris MoU Website www.parismou.org
Calculated taking in account previous 3 years
Calculated each year Renewed every 1st of July
RO Performance is the RO, not the Class
Paris MoU calculation, not the EU Directive
Renewed annually on 1st July

## Slide 19: How can Company be High Performance?
Must have Deficiency Index below average
Must have Detention Index below average
Only possible if no banning of any of the ships in last 36 months

## Slide 20: Company Performance
Detention Index | Deficiency Index | Company Performance
Above Average | Above Average | Very Low
Above Average | Average | Low
Above Average | Below Average | 
Average | Above Average | 
Below Average | Above Average | 
Average | Average | Medium
Average | Below Average | 
Below Average | Average | 
Below Average | Below Average | High
If no Inspections, Company Performance is Medium

## Slide 21: Determine Company Indexes
Detention Index
5.5 % det./insp.
Below Average
On Average
Above Average
7.5 % det./insp.
3.5 % det./insp.
- 2
+ 2
Deficiency Index
3.9 points/insp.
Below Average
On Average
Above Average
5.9 points/insp.
1.9 points/insp.
- 2
+ 2
20
4.4
If banning, Detention Index is Above Average

## Slide 22: Inspection Priority
Priority II
Ship may be inspected
Inspection Window
Priority I
Ship must be inspected
Overriding Factors
Unexpected Factors
Priority I
Priority II
But…
If not inspected within Window, ship becomes
... MS still may inspect outside the regime!

## Slide 23: Overriding Factors (triggers PI)
Ships reported by another Member State Excluding Unexpected Factors
Collision, grounding or stranding
Discharge of harmful substances or effluents
Erratic or unsafe manoeuvring whereby routing measures adopted by IMO, or safe navigational practices and procedures not followed
Class suspension/withdrawn for safety reasons after last PSC inspection
Ships not identified in the database
Notes: 5 and 6 are automatic
BR 1518 and 1519

## Slide 24: Unexpected Factors (triggers PII)
Ships reported by pilots or relevant authorities
Fail to comply with reporting obligations ETA
Outstanding deficiencies Only for Code 15 (rectify at next port) and 18 (rectify in 3 months)
Previously detained more than 3 months ago
Complain from crew, person or organization with legitimate interest Safe operation, living/working conditions and pollution
Ship operated in a manner to pose a danger
Reported cargo problems Noxious or dangerous cargo in particular
Presumption of SRP higher than the provided by THETIS
Certificates by a formerly (PMoU) RO where recognition was withdrawn
Notes: List of unexpected factors as per MoU text Annex 8
The list of unexpected factors as per Directive 2009/16/EC Annex I 2.B is slightly different worded

## Slide 25: SRP Inspection Window
12th month
10th
HRS
SRS
LRS
6th month
Date of last
Inspection
PII
PI
PI
PII
PI
PII
5th
36th month
24th
Notes: Inspection Resets the Clock

## Slide 26: NIR: Fair Share
How many ships MSs have to Inspect per year?
  1st Calculate Regional Commitment
  2nd Calculate MS Inspection Share

## Slide 27: NIR: What if can’t Postpone neither Inspect?
Counts as a Miss for member state!
  MS can miss up to 5% of PI HRS
  MS can miss up to 10% of PI SRS/LRS

## Slide 28: NIR: But if…
Member States’ ports can be called by:
PI ships > Inspection Share Over-burdened
PI + PII ships < Inspection share Under-burdened

## Slide 29: NIR: But if…
Are you Overburdened!?
  Inspect PI = Inspection Share
  MS can miss up to 30% of PI
Are you Under-burdened!?
  Inspect all PI (can still miss 5% HRS and 10% SRS/LRS)
  MS comply doing at least 85% of PII
... make sure that misses are justified …

## Slide 30: Fair Share

## Slide 31: Reporting Obligations
72H Before ETA if eligible for Expanded Inspection PSC Directive (2009/16/EC) – Article 9 and Annex III
24H Before ETA for every ship VTM Directive (2002/59/EC) – Article 4
ATA and ATD within a reasonable time PSC Directive (2009/16/EC) – Article 24.2
Notes: There is Tonnage limitation for the VTM Directive, but not for the PSC Directive

## Slide 32: Type of Inspections - Where to look
Initial inspection PSC Directive (2009/16/EC) – Article 13.1
More detailed inspection PSC Directive (2009/16/EC) – Article 13.3 and Annex V
Expanded inspection PSC Directive (2009/16/EC) – Article 14 and Annex VII and the Implementation Regulation 428/2010

## Slide 33: Type of inspections
HRS or LRS/SRS of a Risk Type and >12 yrs
LRS/SRS not (of a Risk Type and >12 yrs)
Initial
MD
EI
Periodic + Additional
-
-
Periodic
-
-
* According to the professional judgement
Additional
-
*
Initial
MD
EI
Additional
-
-
Periodic + Additional
-
-
Periodic
-
Notes: This 2 tables show which type of inspection has to be carried out depending on the Ship Risk Profile in case of a periodic or additional inspection or a combination of both
THETIS always advise
Additional inspections will reset the time window.

## Slide 34: Postponement Possibilities for PI Ships
MS A
MS B
Paris MoU Region
PI Ship will call at MS A
Same MS
Different Port
Within 15 days
Calling Port outside PMoU
Return to Same MS
Within 15 days
Other PMoU MS
Agreed in advance
Within 15 days
(…)

## Slide 35: Refusal of Access (Banning)
-36 months
-24 months
-12 months
Today
Detained or PoO 3 or more times
Detained or PoO 3 or more times
OR…
Jumped detention
Failed to call to agreed repair yard

## Slide 36: Multiple Banning – 1st Ban (Example for Black Flag. Grey Flag is 2 yrs)
3 years
D/PoO
D/PoO
1st Ban
D
3 months
Ship was never banned

## Slide 37: Multiple Banning – 2nd Ban (Example for Black Flag. Grey Flag is 2 yrs)
3 years
D/PoO
D/PoO
2nd Ban
D
12 months
Ship was banned once (since 17/06/2009)

## Slide 38: Multiple Banning – 3rd Ban
3rd Ban
D
24 months
Flag is on the White List
RO is Recognized by one PMoU MS
Company is High Performance
For the ban to be lifted:
Ship was banned twice (since 17/06/2009)

## Slide 39: Multiple Banning – 4th Ban – Permanent
4th Ban
Permanent Ban
D
Ship was banned tree times (since 17/06/2009)

## Slide 40: Multiple Banning (Example for Black Flag. Grey Flag is 2 yrs)
3yrs
3yrs
D/PoO
D/PoO
Ban
Ban
Ban
Ban can be lifted after 3 months
Ship Banned 2nd time when detained after 2 detentions/PoO
in 3 years
Ban can be lifted after 12 months
Ship Banned 3rd time if detained
Ban can be lifted after 24 months if:
  White Flag +
  RO PMoU Recog. +
  HP Company
  Or Permanent Ban
D
D
D
Ship Banned 1st time when detained after 2 detentions/PoO in 3 years
D
Permanent Ban
Permanent Banned if detained

## Slide 41: Not counting for multiple detentions
Banning because of jump detention
Banning because of not reaching the agreed repair yard

## Slide 42: Appeal against Detention or Ban
National Law
Port State
APPEAL
REVIEW
Review Panel
NIR
Revoke
Confirm
Flag/RO
Owner/Operator
2009/16/EC
Article 20
If Appeal, Review will not be considered
Paris MoU Advises the Port State

## Slide 43: Training of PSC Officers
Scheme to
harmonise the
level of Professional
Competency in Paris MoU
Training tools
PSCO tools
MS
EMSA
Paris MoU
Mandatory training for New Entrant and Authorised PSCOs

## Slide 44
Thank you!