## Slide 1
SSN-LRIT Training Course for Croatia
The SSN V2 System
12-13 June 2012
Zagreb

## Slide 2: SSN presentation: content
Architechture
Type of information exchanged
Users
How to notify and search for information?
    PortPlus
    Incident report
    MRS & AIS
  Ship activity tracking
        Another means to retrieve information: SSN graphical Interface (SSN GI)
2

## Slide 3: Mandatory information exchanged through SSN
Ship notifications (AIS and MRS - sent when ships are in mandatory reporting areas)
Incident reports (Member State information submitted about accidents and incidents which occur at sea e.g SITREP, POLREP etc…)
Port Plus notifications: Pre-arrival (72h - 24 hours ), Arrival and Departure
Hazmat notification (information on dangerous and polluting goods on board ships - embedded in PortPlus)

## Slide 4: Information exchanged through SSN
Port A
Port B
Pre-arrival
Ship ID, ETA, ETD, POB etc…
Ship report
AIS/MRS
ID, POB, Position…
HAZMAT
Ship ID, ETD, ETA, Cargo
Incident/accident
Polrep,
Sitrep,
Lost&Found Container
Waste
Other …
x
x
x
AIS track
Ship ID +
Arrival (ATA)
PortPlus message
Departure (ATD)

## Slide 5: SSN reporting: why is it important?
Legal obligations (Directives VTMIS-2002/59 – PSC 2009/16)
Data is used by other Member States:
  In SAR operations- Persons on Board and HAZMAT
  to get an early warning on vessels posing potential risk
Data can be used to improve maritime traffic image and related information:
  Confirm where the vessel is (real time position)
  Confirm ETA
  Obtain lists of ships in Ports
  Obtain reliable statistics

## Slide 6: Users of the system
National Competent Authorities in the Member States decide which national users can access the system.
There are currently around 3.000 users identified
Users (VTMIS) include:
  Maritime administrations
  Ports
  Vessel traffic Services
  Maritime Rescue Coordination Centres (MRCC)
  Coast Guards
  Pollution survey centres
  PSC Officers

## Slide 7: Access rights matrix
ROLES ACCESS RIGHTS |  | NCA | NCA ADMIN | CST | POR | PSC | OTH
Data Providing | Port call | X [country] | X [country] | X [country] | X [port] | X [country] | X [country]
 | Hazmat | X | X | X | X | X | X
 | MRS position | X | X | X |  |  | X
 | AIS position | X | X | X |  |  | 
 | Incident | X | X | X | X | X | X
Data Requesting | Port call | X | X | X | X [port] | X | X
 | Hazmat | X | X | X | X [port] | X | X
 | MRS position | X | X | X | X [port] | X | X
 | AIS position | X | X | X | X | X | X
 | Incident | X | X | X | X | X | X
 | Ship IDs | X | X | X | X | X | X

## Slide 8
8
SSN
core
SSN
Streaming interface
Regional server
(Med)
NCA
NCA
Notifications
(Dangerous goods, alert,
Port notification)
Regional server
(Baltic /North Sea)
Back
SafeSeaNet, how does it work?
Request
(to SSN central)
Request for details
(to the owner)
Response
NCA
LRIT

## Slide 9: How and when to notify? How to retrieve information?
PortPlus notification
  What? How and to whom?
Incident reports
  Purpose
  Types of Incident Reports
  Distribution
Ship notification
MRS
AIS
D. Searching information

## Slide 10: PortPlus Reporting Obligations (PSC+VTMIS) HAZMAT non EU
ATA
ETA - 24 H
ETA - 72 H
ATD
THETIS
Hazmat
Non- EU
SafeSeaNet (Central)
Port A
SafeSeaNet (National)
SSNUsers in other Member States

## Slide 11
ATA
24 H
72 H
ATD
THETIS
SafeSeaNet (National)
Port A
ATD+ HAZMAT
(on departure)
PortPlus Reporting Obligations (PSC+VTMIS) HAZMAT EU
Port B
SafeSeaNet (Central)
SafeSeaNet (National)

## Slide 12: Note
The WEB interface we use hereunder for demo purposes is that of the Central SSN, not that of the national or local system. The SSN Central system can be used for retrieving data, notifying incidents and as backup for sending data.

## Slide 13: Login using your credentials
1. Your credentials
Login with single window

## Slide 14: Start with SSN V2
1. Your login
2. Click on Send Notification

## Slide 15: PortPlus notification
3. Enter IMO number of the vessel
4. Enter port of call
Note: Most of the functionalities in SSN will start with selection of the specific ship from SSN Ship Data base. SSN Ship Data base consists of vessel ids provided by Member States in notifications, and is validated by Maritime Support Services.

## Slide 16: PortPlus notification
5. Click on the button and provide a new voyage

## Slide 17: PortPlus notification
6. Fill in details and submit notification

## Slide 18: Searching for data in SSN v2
2. A new tab will open
1. Go to Find Information

## Slide 19: Searching for port and Hazmat information
Search using… | Which query? | What you can get?
Ship identifiers | List Expected calls of Selected Ship | Where is it going to arrive (PORTs)? When (ETAs)?
 | Expected Call Of Selected Ship | Where is it going to arrive (PORT)? When (ETA)? Is HAZMAT on board?
 | Most Recent Arrival Of Selected Ship” | Where the ship has arrived (PORT)? At what time (ATA)? Is HAZMAT on board?
 | Most Recent Departure Of Selected Ship | From where the ship has departed (PORT)? At what time (ATD)? Is HAZMAT on board?
 | Recent And Current Ship Calls Of Selected Ship | Where the ship was (PORTs)? At what time departed? (ATDs, ATA)
 | Latest registered Ship Call Data of Selected Ship | Most recent update related to the ship calls, including HAZMAT information

## Slide 20: Searching for port and Hazmat information
Searching using… | Which query? | What you can get?
Port identifiers | Expected ship calls at EU Port | Vessels and ETAs of all expected ships in a Port
 | Current Ship Calls at EU Port | Vessels and ATAs of ships in Port
 | Completed Ship Calls At EU Port | Vessels and ATAs, ATDs and Next Ports of vessels which left port
Latest call updates | Latest Call Updates | All updates of Port + within selected period of time
 | Latest Call Info At Specific Port | All updates of Port + for the selected port
Call updates historical search | Ship Calls Registered By SSN Yesterday | Ship calls registered within the previous calendar day
Search using ShipCallID * | ShipCallID search | List of Port+ notifications

## Slide 21: Searching for data in SSN v2
1. Expand Voyage Ship Notifications
2. Select relevant query

## Slide 22
Ships considered as:
“Posing a potential hazard to shipping or a threat to maritime safety, the safety of the individuals or the environment”; detected by any MS (Article 16 1 of Directive 2002/59 sets out the criteria for defining such ships (see the types of IR hereafter, section 3.)
Have to be reported to the authorities on the planned route of the ship (Art 16.2 of Directive 2002/59) and the Flag State.
“WARNING” purpose
Incident Report (IR) – Main purpose

## Slide 23: IR, distributed or not?
IR distributed to relevant MS + Flag
According to art 16.2
Prior assessment: Is the information relevant? Could the incident have an effect on shipping safety or in the environment in the waters of other MSs?
Ship underway or authorised to sail
Destination known, only exceptionally distributed to all MSs
Too many = contrary effect
IR notified to SSN central system
According to art 21.1 and 17
SSN contains a repository of IRs up to 5 years as agreed by the SSN Group
Information to be used in a routine basis. For a single ship we may find:

## Slide 24
A ship notifies an incident on board to a Coastal Station
IRs distribution
Planned route of the ship

## Slide 25
Member States along the route have to be notified
IRs distribution

## Slide 26: Incidents reports – 1. SITREP
SITREP - Reports related to ship’s safety and seaworthiness
Example:
A vessel runs aground close to port A and is re-floated with assistance. A temporary repair is made and the ship is allowed to proceed to a yard (located in port B in a different country) where further repairs are expected to be carried out. A SITREP should be distributed by port A at the latest at the time of departure, communicating the information to MSs along the ship’s planned route towards port B.

## Slide 27: Incidents reports - 2. POLREP
POLREP - incident reports related to pollutions (proved or presumptive evidence)
Example:
  An environmental patrol flight reports a vessel which is discharging cargo residues, other cargo associated waste or garbage. A POLREP should be sent to the central SSN system for distribution to the relevant MSs along the planned route of the ship (if known). The notification should contain any relevant information on the ship, its location and the cargo.

## Slide 28: Incidents reports - 3. Waste
Waste - incidents reports related to the non provision of waste deliveries (Art. 12.3 Dir. 2000/59/EC)
Example:
A ship leaves the port without having complied with articles 7 or 10 of Directive 2000/59/EC; this means a clear non-compliance with the mandatory delivery of ship generated waste or cargo residues to a port reception facility, if no evidence was provided that, in relation to the scheduled voyage, there was sufficient dedicated storage capacity for all the ship generated waste till the next port of call.

## Slide 29: Incidents reports - 4. Lost and Found Containers
Lost and Found Containers and packages incident
reports
Example:
A container carrier reports to the nearest coastal station that it has lost some of its deck containers during severe weather conditions.
The MS receiving the information should distribute it to all potentially affected MSs.

## Slide 30: Incidents reports-5. Other reports 1/6
Other reports: Ships which have failed to comply with the reporting requirements of Directive 2002/59;
Example:
A ship did not report to a coastal station any of
the report required by Article 17 (e.g a SITREP).
An awareness incident report should be
distributed to the coastal stations located along
the planned route of the vessel.

## Slide 31: Incidents reports -5. Other reports 2/6
Other reports: Ships which have failed to comply with the applicable rules in ships’ routeing systems and VTS;
Example:
A vessel contravenes the reporting rules during its transit through a declared VTS area. An Incident Report message should be distributed to the MSs along the planned route of the vessel.

## Slide 32: Incidents reports -5. Other reports 3/6
Other reports: Ships which have been refused access to ports of the Member States;
Example:
A ship which has a refusal of access order (“banned”) on the Paris MoU list is passing the MRS of a MS. The MS, even if the ship is not calling at one of its ports, should send an incident report of the type “other”. As the destination is known, and as the ship will proceed within the areas of responsibility of other MSs, this Incident Report type “Other” should also be distributed along the planned route of the ship (Once the refusal of access order has been lifted, the information should be exchanged through SSN).

## Slide 33: Incidents reports -5. Other reports 4/6
Other reports: Ships which have failed to notify, or do not have, insurance certificates or financial guarantees pursuant to any Community legislation and international rules (e.g Directive 2009/20/EC on the insurance of ship-owners for maritime claims )*
*On hold, pending the validation of the format
Example:
A ship is inspected and no certificate of insurance or other financial security in respect of civil liability for oil pollution damage is found on board by the inspector. The Coastal Station, as defined in Directive 2002/59, should distribute an Incident Report providing the information concerned. This Incident Report shall be sent to those MSs along the planned route of the ship.

## Slide 34: Incidents reports -5. Other reports 5/6
Other reports: Ships reported by pilots or port authorities as having apparent anomalies which may prejudice their safe navigation or create a risk for the environment*.
*On hold, pending the validation of the format
Example:
The Pilot Service of a Port in MS A detects a problem in the steering gear of a ship when departing. This information, communicated to the relevant authority in MS A, has to be sent by this authority to the MSs along the planned route of the ship using an incident report type “other”.

## Slide 35
  Actions undertaken by MS: following Article 16.3 of Directive 2002/59/EC
Example:
A ship did not report when entering a MRS area of Member State A and did not answer to VHF calls. Through SSN the available information confirmed that the ship was expected at a Port X (MS B). An incident report type “other” (Ships failed to comply with the applicable rules in ships’ routeing systems and VTSs operated within the responsibility of a MS) has been sent by MS A and distributed on the planned route of the ship. The destination MS B decided to carry out an inspection. The findings are reported to the MS A though an incident report “actions undertaken by MS”.
Incidents reports -5. Action taken 6/6

## Slide 36: IR via central SSN web
E-mail alert
Distribute?
Notify
Store
1
2
3
4

## Slide 37: Notifying Incident reports
2. Choose e.g. SITREP
3. Select vessel
1. Go to Send Notifications
1

## Slide 38: Notifying incident reports
5. Provide all descriptions and position, or
6. or, Upload the document
4. Fill in details
1

## Slide 39: Distribution
7. SSN wil ask you for voyage details to calculate route and propose automatically the list of recipients along the planned route
8. Select list of recipients
9. Finish the process by submitting the alert
3

## Slide 40: Email Sent to the recipients - example
4

## Slide 41: You are a recipient of a distributed IR
Once you receive the email, follow the link, log in and this page will be displayed:
Click!

## Slide 42: You want to know historical data
1
2

## Slide 43
Incident report in SSN ?……
or not Incident report in SSN?......
Please consult the IR guidelines

## Slide 44: Ship Notification
AIS notified:
As a stream (IEC)
Via XML
MRS notified:
- Via XML

## Slide 45: Ship Notification
MRS (art. 5, VTMIS Directive)- in red included in notification -
A. ship identification (name, call sign, IMO identification number or MMSI number),
B. date and time,
C or D. position in latitude and longitude or true bearing and distance in nautical miles from a clearly identified landmark,
E. course,
F. speed,
I. port of destination and estimated time of arrival,
P. cargo and, if dangerous goods present on board, quantity and IMO class,
T. address for the communication of cargo information,
W. total number of persons on board,
X. Miscellaneous:
characteristics and estimated quantity of bunker fuel, for ships of more than 1 000 gross tonnage,
navigational status.

## Slide 46: Comparison MRS in SSN/ADRIREP (first report)
In SSN….
  XML protocol already in place
  Access rights : all 27 SSN MS (except port users)
  No update : new notification
  No distribution mechanism
  No departure information (G)
  No Draught (O)
  No ETA next check point (N)
  No size and type (U)

## Slide 47: Ship Activity Tracking
Automatic system in SSN to get a warning (email)
For a selected ship
For a defined period of time
Based on the notifications received by SSN (AIS, MRS, Port+ or Incidents)

## Slide 48: Ship activity tracking - Individual vessels Hands-on (1)
1. Go to “Ship Activity Tracking” and indicate a vessel
2. Click on IMO
3. Click on “Add”

## Slide 49: Ship activity tracking - Individual vessels Hands-on (2)
4. Choose the notification type & recipients
5. Check your e-mails

## Slide 50: SSN GI: another means of retrieving SSN information
General introduction
- Login
- Interface
B. Functionalities
- Enrichment
- Watchdog
- Advanced filters
Conditions of Use
Users’ benefits

## Slide 51
1. Your login
2. Click on SSN GI
Note: STIRES is only an administration console
Login using your credentials

## Slide 52: SSN-GI v2 Interface
There are 344 SSN GI users, of which:
326 are VTMIS users,.
18 are Non-VTMIS users

## Slide 53: Enrichment data in SSN GI
1. Click on specific vessel to get enrichment data

## Slide 54: Enrichment data in SSN GI
2. Click on vessel e.g. with HAZMAT
3. Switch to enrichment tab

## Slide 55: Enrichment data in SSN GI
4. Enrichment (EIS) data availability is indicated with blue links tab
5. Click on the link to get the information about HAZMAT cargo on- board
6. Request window will appear – request detail
7. Go to the right bottom corner to check details when the response message arrives

## Slide 56: Enrichment data in SSN GI
8. Choose Notifications tab in the pup-up window
9. Select and double click the details of the HAZMAT cargo
10. Read details of the HAZMAT cargo on board

## Slide 57: Watchdog functionality in SSN GI
1. Choose Passage Line – area from the Tools option
2. New window will appear
Note: User will have to start by defining an alerting area
3. Click on NEW to define your area for alerting
Notes: Setup an alerting area and get a warning and even e-mail for passing vessels

## Slide 58: Watchdog functionality in SSN GI
4. Choose the type of the area: line or polygon, edit the name and switch to “Points list” tab
5.Enter coordinates or tick the box to select points from the map
6. Draw an area and double –click on the last point

## Slide 59: Watchdog functionality in SSN GI
7. After defining area move to “Watchdogs” tab
8. Click on “Add”
9. Describe your area and select one of the created areas
10. Tick on “Warning” to define, how you would like to be warned
11. Define the type of alert you would like to receive- pop-up or e-mail

## Slide 60: Watchdog functionality in SSN GI
12. Once the Watchdog is saved, activate it
13. Select it and press “ON”
14. For each passing vessel you will receive warning and e-mail alert, as well as the list of the passing vessels will be updated
Note: Updates Icon is available via Watchdog menu or in the bottom right corner

## Slide 61: Advanced filters functionality
1. After clicking on NEW FILTER fill in the name and description and remember about new elements for vessels preferences
2. Upon clicking on preferences of filter type user will be given with new export tool
3. Go to advanced lists tab.

## Slide 62: Advanced filters functionality
4. Click on import and select csv file location
5. Filter will apply only to selected vessels
Filters can be saved as new and as existing versions
Advanced lists can be imported from .csv file to fulfil individual needs
User can setup validity time and refresh interval per each filter

## Slide 63: SSN GI Condition of Use
Chart property rights
…Users of the charts provided by STIRES Web service shall NOT copy, duplicate, distribute data or materials…
Raw AIS data provision
…the AIS data provider is responsible for the quality of the AIS raw data provided to STIRES…
Data use and distribution
…The SSN data provided through the STIRES interface shall be used for the purposes and in accordance with the general concept for SSN as defined in VTMIS Directive…
…The participating state acting as data requesters of the STIRES module shall also be data provider…
…The same access rights established for SSN shall be applied for the data accessible through STIRES from the SSN EIS following the enrichment process…

## Slide 64: SSN Technical documentation
http://www.emsa.europa.eu/documents/technical-documentation

## Slide 65: How to join the SSN system and start operating?
ADMINISTRATIVE PROCEDURES
SafeSeaNet Welcome on Board document
Updating the NCA, NCA 24/and LCA details
Creating an account for the NCA user/LCA users
TECHNICAL PROCEDURES
Possible use of training site for national tests
Commissioning Tests (reservations, scenarios)
Request for the Digital Certificate

## Slide 66: SSN users benefits
MRCC Centres
  Number of persons on board for SAR operation:
  Last position of a ship (AIS or more sensor)
  Ships in the area (based on AIS, LRIT etc…)
  Estimation of potential pollution (hazmat details)
Maritime Assistance Services (MAS)
  Hazmat information and incident history
  The general benefit of the SSN Graphical interface is the enrichment. It is the only tool dispaying AIS tracks with relevant SSN notification attached to these tracks.

## Slide 67: SSN users benefits
Port Authorities
  Support to the management of port entries
  Be aware of incidents or accidents for ships bound to their ports
VTS Centres
  Cross checking Hazmat information:
  Vessel posing a risk (e.g. involved in collision)
  Reduce the questioning of ships (by VHF)
Other administrations
- Picture of the marine traffic

## Slide 68: The end
Thank you for your attention